## Slide 1
System Size
9,856 nodes 77 compute racks 128 AMD nodes per rack
39,424 total GPUs
Compute Node
1 64-core AMD EPYC CPU
4 AMD MI250X GPUs
4 HPE Slingshot 200 Gbps NICS
System Interconnect
HPE Slingshot Ethernet with a 3-hop Dragonfly Topology
Storage
700 PB HDD+11 PB Flash, 9.4 TB/s
10 PB Metadata Flash Lustre
3.8 TB node-local NVMe per Frontier node
Node Performance
214 TF double precision
Notes: Debuting in 2022 as the world’s fastest, Oak Ridge National Laboratory’s Frontier supercomputer is the world’s first exascale system. Frontier has reached 1.353 EF LINPACK. ORNL’s long history of supercomputing excellence enables scientists to expand the scale and scope of their research, solve complex problems in less time, and fill critical gaps in knowledge.
System Size
9,856 nodes
77 compute racks (8,000 lbs each)
128 AMD nodes per rack
Compute Node
1 64-core AMD “Optimized 3rd Gen EPYC” CPU
4 AMD Instinct MI250X GPUs
4 HPE Slingshot 200 Gbps (25 GB/s) NICs providing a node-injection bandwidth of 800 Gbps (100 GB/s)
GPU Architecture
39,424 GPUs, each feature 2 Graphics Compute Dies (GCDs) for a total of 8 GCDs per node
System Interconnect
HPE Slingshot Ethernet with a 3-hop Dragonfly Topology
High-Performance Storage
700 PB HDD+11 PB Flash Performance Tier, 9.4 TB/s
10 PB Metadata Flash Lustre
3.8 TB node-local NVMe per Frontier node (Two 1.9 TB drives per node)
In aggregate, there is 36PB of total node-local capacity, that can can see performance of ~66TB/s read and ~62 TB/s write36 PB of node local SSD, 66 TB/s read, 62 TB/s write
Programming Models
MPI, OpenMP, OpenACC, OpenCL, DPC++, HIP, RAJA, Kokkos, and others
Node Performance
214 TF double precision